## Slide 1: Representation of Numbers and Characters
Course Code: COE 3205
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | 02 | Week No: | 02 | Semester: | Spring 21-22
Lecturer: | Mst. Tasnim Pervin tasnim.pervin@aiub.edu |  |  |  | 
Course Title: Computer Organization & Architecture

## Slide 2: Lecture Outline
Number System
Conversion Between Number Systems
Addition and Subtraction
Integer Representation in computer
Character encoding and usage by computer (ASCII Code)

## Slide 3: Number System
Topic sub heading..
Decimal Numbers
Binary Number system
Hexadecimal Number system

## Slide 4: Number System
Decimal Numbers
In a positional number system
  Each digit in the number is associated with a power of 10.
  i.e.3245 = 3 thousands, 2 hundreds, 4 tens and 5 ones.
  OR, 3245 = 3X(10^3)+2X(10^2)+4X(10^1)+5X(10^0)
In a positional number system
  A number b is selected as the base
  Symbols are assigned to numbers between 0 and b-1
  In decimal system symbols are 0,1,2,3,4,5,6,7,8,9.
  The base ten is represented as 10

## Slide 5: Number System
Binary Number System
The base is two
There are only two digits, 0 and 1.
i.e. binary string 11010 represent the number 1X(2^4)+1X(2^3)+0X(2^2)+1X(2^1)+0X(2^0) = 26
      Base two is represented in binary as 2

## Slide 6: Number System
Why Hexadecimal?
We have decimal and binary. Why Hex?
Binary:
  Numbers written in binary tend to be long and difficult to express
  16 bits are needed to represent a word in 8086-based computer.
Decimal:
  Difficult to convert into binary.
  *** Thus a third number became necessary

## Slide 7: Number System
Hexadecimal Number System
The base is sixteen
There are total sixteen digits: 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
i.e. hex digit 4A represent the number:
  4X(16^1)+ AX(16^0) = 74
  Base sixteen is represented in hex as 16
Conversion between binary and hex is easy
Sixteen is = 2^4, So each hex digit corresponds to a unique four-bit number.

## Slide 8: Number System
Decimal, Binary and Hex Numbers

## Slide 9: Conversion Between Number Systems
Binary to decimal
Decimal to Binary
Hexadecimal to Decimal
Decimal to Hex
Hex to Binary
Binary to Hex

## Slide 10: Conversion Between Number Systems
Decimal to Binary
Convert the Decimal number 25 in Binary.

## Slide 11: Conversion Between Number Systems
Hexadecimal to Decimal
Convert hex number 589 into decimal number.
    =5*(16^2)+8*(16^1)+9*(16^0)
    = 1280+128+9
    = 1417

## Slide 12: Conversion Between Number Systems
Decimal to Hex
Convert 415 to Hex

## Slide 13: Conversion Between Number Systems
Hex to Binary
Convert 39A2h to Binary

## Slide 14: Conversion Between Number Systems
Binary to Hex
Convert the Binary number 1000011001000011 into Hex
1000 0110 0100 0011
8 6 4 3
Convert the Binary number 10010010010001001101011011111 into Hex

## Slide 15: Conversion Between Number Systems
Conversion Task: Binary and Hex to Decimal
          1110b
          100101011101b
          46Ah
          FAE2Ch

## Slide 16: Conversion Between Number Systems
Conversion Task: Decimal and Hex into Binary
          97
          627
          A2Ch
          B34Dh

## Slide 17: Addition and Subtraction
          Hex Addition
          Binary Addition
          Hex Subtraction
          Binary Subtraction

## Slide 18: Addition and Subtraction
Hex Addition Table

## Slide 19: Addition and Subtraction
Hex Addition
Add hex number 5B39h with 7AF4h
  In Unit’s column 9h+4h=13d=Dh
  In next column, 3h+Fh=12h, we write 2 and carry 1
  In next column, Bh+Ah+ 1h (from previous carry)= 16h , we write 6 and carry 1
  Finally, in last column, we compute, 5h+7h+1=Dh
thus, if we combine it all,
5B39h
7AF4h
=====
D62Dh

## Slide 20: Addition and Subtraction
Task: Hex Addition
Solve the following:
            B23CDh + 17912h
            FEFFEh + FBCADh

## Slide 21: Addition and Subtraction
Binary Addition
Add binary number 100101111b with 110110b
    add some padding Zero with small number. So 110110b becomes 000110110b
    In Unit’s column 1b+0b=1b
    In next column, 1b+1b=10b, we write 0 and carry 1
    In next column, 1b+1b+1b (from previous carry)= 11b , we write 1 and carry 1
    In next column, 1b+0b+1b (from previous carry)= 10b , we write 0 and carry 1
    In next column, 0b+1b+1b (from previous carry)= 10b , we write 0 and carry 1
    In next column, 1b+1b+1b (from previous carry)= 11b , we write 1 and carry 1
    In next column, 0b+0b+1b (from previous carry)= 1b , we write 1 and No Carry
    In next column, 0b+0b+No carry = 0b
    In Last column, 1b+0b = 1b
    thus, if we combine it all,
  100101111b
  000110110b
  =========
  101100101b

## Slide 22: Addition and Subtraction
Task: Binary Addition
Solve the following:
  100101b+10111b
  100111101b+10001111001b

## Slide 23: Addition and Subtraction
Subtraction: Hex
Subtract hex number BA94h from D26Fh
  In Unit’s column Fh-4h=11d=Bh
  In next column, 6<9 so, we must borrow 1 from the third (right to left) column. Thus, 16h-9h=?
        16h-9h = Dh, (Looking at Hex addition table, D+9=16
        Or, Hex numbers are A…F,10,11,12,13,14,15,16h/22d - 9d/h = 14d/Dh
  In next column, 12h-Ah-1(previously lend one) = 12h/18d-10d-1d/h = 7h
  In next column, Dh-Bh-1(previously lend one) = Dh/13d-11d-1d/h = 1h
  thus, if we combine it all,
D26Fh
- BA94h
=====
17DBh

## Slide 24: Addition and Subtraction
Task: Hex Subtraction
Solve the following:
            5FC12h-3ABD1h
            F001Ch-1FF3Fh

## Slide 25: Addition and Subtraction
Task: Binary Subtraction
Solve the following:
          11011b-10110b
          10000101b-111011b

## Slide 26: Integer Representation in computer
Hardware of a computer restricts the size of a number can be stored.
lsb = least significant bit [Right most bit or bit 0]
msb = most significant bit [left most bit or bit 15]

## Slide 27: Integer Representation in computer
Unsigned integers
Unsigned integers: Non-negative integer
The largest unsigned integer of a byte= 11111111b or 255d or FFh
The largest unsigned integer of a word= 1111111111111111b or 65535d or FFFFh
*** if LSB of an integer is 1 then its ODD . However, if it is 0 then Even

## Slide 28: Integer Representation in computer
Signed Integer
Signed Integer: Can be positive or negative number
The MSB is reserved for the sign
MSB =1 [Negative]
MSB =0 [Positive]
*** Negative integers are stored in a computer using TWO’s complement

## Slide 29: Integer Representation in computer
One’s Complement
Ones complement is obtained by complementing each bit.
      i.e. replacing 0 by a 1 and 1 by a 0.
  To find the one’s complement of 5 or 0000000000000101 [16bit representation of 101]
    1111111111111010 [complementing each bit]

## Slide 30: Integer Representation in computer
Two’s Complement
  To get Two’s Complement,
    Add 1 to the one’s complement of a number
    Thus, Two’s complement of 5 is
    1111111111111010 [one’s complement of 5]
    +1
    —————————
    1111111111111011 [Two’s complement of 5]

## Slide 31: Integer Representation in computer
Two’s Complement- Observation
If we add two’s complement of 5 with it, we get
  1111111111111011
  0000000000000101 ===============
  10000000000000000
  We get total 17bits here, however, word bits can hold only 16bits.
  Thus the carried out MSB 1 is lost and final result is 0
  5 +(-5) also results zero.
  Adding a number N and ones complement gives 16 one’s
  Adding a number N and Two’s complement gives 16 zero’s

## Slide 32: Integer Representation in computer
Two’s Complement- Task: 8/16bit Representation
Find the two’s complement of the two’s complement of 5.
Show how the following decimal integer would be represented in
      a) 8 bits b)16bits. [express the result in hex]
        -97
        -120
        -40000
        -128
        65536

## Slide 33: Integer Representation in computer
Two’s Complement- Task
Give 16-bit representation of each of the following integers and express the result in hex:
              234
              -16
              31634
              -32216

## Slide 34: Integer Representation in computer
Subtraction as Two’s Complement Addition
If AX contains 21FCh and BX contains 5ABCh, find AX-BX
    AX=21FCh = 0010000111111100
    BX= 5ABCh = 0101101010111100
    O’C of 5ABCh = 1010010101000011 [one’s complement]
    +1
    ===================
    1010010101000100 = A544h [1 is carried and lost]
    Now, AX+BX=21FCh+A544h = C740h
Notes: 1010010101000100

## Slide 35: ASCII Code
ASCII Table

## Slide 36: ASCII Code
ASCII in detail
ASCII code system Uses 7bits = 2^7 =128 to code each character.
Codes from 32 to 126 = 95 characters are only printable.
** to display the character A on the screen, a program sends the ASCII code 41h to the screen.
If we type “RG 2z” in computer, it will process like following:
Address | Character | ASCII Code | Content
0 | R | 52 | 0101 0010
1 | G | 47 | 0100 0111
2 | Space | 20 | 0010 0000
3 | 2 | 32 | 0011 0010
4 | z | 7A | 0111 1010

## Slide 37: Topic Heading..
Task: String Processing in a Computer
If we want to print “Hello World” on the screen, How the memory will look like ?
[Hint: Find ASCII code, content of string from the ASCII table and order them in a address sequence].

## Slide 38
Books
Assembly Language Programing and Organization of the IBM PC
Ytha Yu
Charles Marut

## Slide 39
References
Number Systems Introduction - Decimal, Binary, Octal, Hexadecimal & Conversions
    https://www.youtube.com/watch?v=L2zsmYaI5ww&t=1435s
Hex Addition, Subtraction
    https://www.youtube.com/watch?v=y0B6tuC6niE
    https://www.youtube.com/watch?v=3mV7q3_OAGM
Binary Addition , Subtraction
    https://www.youtube.com/watch?v=TaQS3qSDXV0
Two’s Complement
    https://www.youtube.com/watch?v=_7RK3rsfQ8w
ASCII Code
    https://www.youtube.com/watch?v=KYEDJChGxh8
    youtube.com/watch?v=5aJKKgSEUnY